## Slide 1: Routing Security Roadmap
Job Snijders
NTT Communications
job@ntt.net
This presentation contains projections and other forward-looking statements regarding future events or our future routing performance. All statements other than present and historical facts and conditions contained in this release, including any statements regarding our future results of operations and routing positions, business strategy, plans and our objectives for future operations, are forward-looking statements (within the meaning of the Private Securities Litigation Reform Act of 1995, Section 27A of the Securities Act of 1933, as amended, and Section 21E of the Securities Exchange Act of 1934, as amended). These statements are only predictions and reflect our current beliefs and expectations with respect to future events and are based on assumptions and subject to risk and uncertainties and subject to change at any time. We operate in a very competitive and rapidly changing environment. New risks emerge from time to time. Given these risks and uncertainties, you should not place undue reliance on these forward-looking statements. Actual events or results may differ materially from those contained in the projections or forward-looking statements. Some of the factors that could cause actual results to differ materially from the forward-looking statements contained herein include, without limitation: (i) the contraction or lack of growth of markets in which we compete and in which our products are sold (ii) unexpected increases in our expenses, including manufacturing expenses, (iii) our inability to adjust spending quickly enough to offset any unexpected revenue shortfall, (iv) delays or cancellations in spending by our customers, (v) unexpected average selling price reductions, (vi) the significant fluctuation to which our quarterly revenue and operating results are subject due to cyclicality in the wireless communications industry and transitions to new process technologies, (vii) our inability to anticipate the future market demands and future needs of our customers, (viii) our inability to achieve new design wins or for design wins to result in shipments of our products at levels and in the timeframes we currently expect, (ix) our inability to execute on strategic alliances, (x) the impact of natural disasters on our sourcing operations and supply chain, and(xi) other factors detailed in documents we file from time to time with the Securities and Exchange Commission. Forward-looking statements in this release are made pursuant to the safe harbor provisions contained in the Private Securities Litigation Reform Act of 1995.

## Slide 2: Why are we doing any of this?
Creating filters based on public data, forces malicious actors to leave a trail in IRR, WHOIS or other data sources: auditability
Bugs happen! – your router may suddenly ignore parts of your configuration, you’ll then rely on your EBGP peer’s filters
Everyone makes mistakes – a typo is easily made

## Slide 3: Average view on routing security
Notes: No filters, or you just email what you’d probably announce, or just as-path filters

## Slide 4: Perception: it is hopeless, too many holes…

## Slide 5
Notes: We simply have to go through them one by one

## Slide 6: Exhaustive list of issues in the current ecosystem
IRRdb / database inaccuracy (stale, autopiloted, non-validated)
IXPs not filtering
Lack of Path Validation
Lack of sufficient and good enough software
Lack of operator experience

## Slide 7: IRR – what is broken what can be fixed?
Some IRRdbs do not perform validation
  Meaning that virtually anyone can create virtually any route/route6 object and sneak those into the prefix-filters
Eleven relevant IRRs not validating: RIPE, NTTCOM, RADB, ALTDB, ARIN IRR, BBOI, BELL, LEVEL3, RGNET, TC, CANARIE
Two solutions:
  Lock the database down (RIPE / RIPE-NONAUTH)
  Filter on the mirror level

## Slide 8: RIPE NWI-5 proposal & implementation
RIPE NCC’s IRR previously allowed anyone to register any non-RIPE-managed space if it had not yet been registered. *DANGER*
The “RPSL” password & maintainer was used for this
Three steps were taken:
Cannot register non-RIPE-managed space any more
All non-RIPE space moved to separate “RIPE-NONAUTH” database
Route/route6 ASN authorization rules have been improved
More info: https://www.ripe.net/manage-ips-and-asns/db/impact-analysis-for-nwi-5-implementation
SOLVED

## Slide 9: RIPE NWI-5 proposal & implementation
RIPE NCC’s IRR previously allowed anyone to register any non-RIPE-managed space if it had not yet been registered. *DANGER*
The “RPSL” password & maintainer was used for this
Three steps were taken:
Cannot register non-RIPE-managed space any more
All non-RIPE space moved to separate “RIPE-NONAUTH” database
Route/route6 ASN authorization rules have been improved
More info: https://www.ripe.net/manage-ips-and-asns/db/impact-analysis-for-nwi-5-implementation
SOLVED

## Slide 10: OK – so current status
Ten relevant IRRs not validating: NTTCOM, RADB, ALTDB, ARIN IRR, BBOI, BELL, LEVEL3, RGNET, TC, CANARIE
Done: RIPE

## Slide 11: ARIN IRR allows anyone to register anything
hanna:~ job$ whois -h rr.arin.net 2001:67c:208c::
% This is the ARIN Routing Registry.
% Note: this output has been filtered.
% To receive output for a database update, use the "-B" flag.
% Information related to '2001:67c:208c::/48AS15562'
route6: 2001:67c:208c::/48
descr: 2001:67c:208c::/48 - Job's net
remarks: Job asked me to steal his net. Honest!
origin: AS15562
mnt-by: MNT-ATTW-Z
source: ARIN # Filtered

## Slide 12: ARIN community recognized this is an issue
Consultation at NANOG and through ARIN-Consult mailing list
https://www.arin.net/vault/resources/routing/2018_roadmap.html
https://teamarin.net/2018/07/12/the-path-forward/
ALMOST SOLVED
“Improve, or kill it”

## Slide 13: OK – so current status
Nine relevant IRRs not validating: NTTCOM, RADB, ALTDB, BBOI, BELL, LEVEL3, RGNET, TC, CANARIE
Done: RIPE, ARIN IRR
How to deal with the remaining nine …. ?
Not all of these are so easily communicated with, not all are really actively managed

## Slide 14: The “IRR” system access
The IRR is access through predominantly two “gateways”
  whois.radb.net (bgpq3 and peval default)
  rr.ntt.net
All mirroring is essentially done with one software: IRRd
Solution: Let’s use the hegemonic duopoly for good!

## Slide 15: Improving security at the ”aggregator”?
RIPE IRR
NTTCOM
RADB
APNIC
…
whois.radb.net
rr.ntt.net
bgpq3
Data sources
Aggregators
Clients

## Slide 16: Proposal: Let RPKI “drown out” conflicting IRR
RPKI can be used for BGP Origin Validation – but also for other things!
A RPKI ROA is sort of a route-object
  It has a “prefix”, “origin” and “source” (the root)
  We can use RPKI ROAs for provisioning BGP prefix-filters
Extend IRRd so that when IRR information is in direct conflict with a RPKI ROA – the conflicting information is suppressed (Github)

## Slide 17: RPKI filter at the aggregators
RIPE IRR
NTTCOM
RADB
APNIC
…
whois.radb.net
rr.ntt.net
bgpq3
Data sources
Aggregators
Clients

## Slide 18: RPKI suppressing conflicting IRR advantages
Industry-wide common method to get rid of stale proxy route objects – by creating a ROA you hide old garbage in IRRs
By creating a ROA – you will significantly decrease the chances of people being able to use IRR to hijack your resource

## Slide 19: OK – so current status
IRRs not validating: no longer relevant
Done: RIPE, ARIN IRR, NTTCOM, RADB, ALTDB, BBOI, BELL, LEVEL3, RGNET, TC, CANARIE
SOLVED
NTT & Dashcare have started a full rewrite of IRRd to make this possible:
https://github.com/irrdnet/irrd4

## Slide 20: ”Filtering at IXPs is hard”
Many IXPs have come to realize their responsibilities to the Internet ecosystem and the commercial benefits of a more secure product.
http://peering.exposed/
  9 out of top 10 IXPs are filtering, tenth will later this year
IXP filtering has become much easier, there are multiple fully featured configuration generators:
  https://www.ixpmanager.org/
  http://arouteserver.readthedocs.io/
BIRD’s hegemony in the route server software is being challenged: OpenBGPD is funded to be able to compete
SOLVED

## Slide 21: Many invalid RPKI routes in DFZ
Ben / Niels talked a bit about this – about 6,000 prefixes in DFZ are “invalid”
Only subset of those become unreachable (because of valid or unknown less-specific)
List: https://as286.net/data/ana-invalids.txt (grep for NONE)
How to get that number down?
  IXPs should take a leading role to support their members/customers
  Route servers can start

## Slide 22: Route servers must begin dropping RPKI Invalids
Route servers by definition provide partial Internet tables
No guarantees whatsoever that a given route will be available via RS
When a route server drops a prefix, worst case scenario is rerouting – not an outage.
Network A
Network B
ISP
Internet Exchange

## Slide 23: Not everyone needs to do RPKI
Because of the centralization of the web, if a select few companies deploy RPKI Origin Validation – millions of people benefit
(google, cloudflare, amazon, pch/quad9, facebook, akamai, fastly, liberty global, comcast, etc…)
I think only 20 companies or so need to do Origin Validation for there to be big benefits…
https://dyn.com/blog/bgp-dns-hijacks-target-payment-systems/

## Slide 24: “RPKI Origin Validation is useless without Path Validation aka BGPSEC”
The lack of path validation can be resolved through two methods:
  Densely peer with each other (Example: Google & Akamai have 126+ facilities in common with each other)
  An AS_PATH blocking mechanisms like “peerlock”
Both effectively are “path validation for 1 hop”
Perhaps “1 hop” already is good enough 

## Slide 25: “There is no healthy software ecosystem”
RIPE NCC Validator v3 is works and actively maintained
NLNetlabs is writing a RPKI Cache Validator (Routinator 3000)
A company I can’t name is secretly writing one too
Almost all serious routing vendors have RPKI support (Cisco, Juniper, BIRD, Nokia, FRR – and more are on the way)
Solution: more users results in better software, start using!
SOLVED

## Slide 26: Timeline
IXPs – start doing RPKI Origin Validation on your route servers now
ISPs / CDNs
  if you are pointing default somewhere, do it now
  If your market is mostly West-Europe, do it now
  If you are transit-free, wait a bit

## Slide 27: We aren’t done yet - Future work
Use the RPKI to publish “peerlock” rules about who are authorized upstreams and who aren’t
  https://tools.ietf.org/html/draft-azimov-sidrops-aspa-verification
  https://tools.ietf.org/html/draft-azimov-sidrops-aspa-profile
Extend the RPKI to replace IRR AS-SETs (IRR / RPKI feature parity)
  https://tools.ietf.org/html/draft-ss-grow-rpki-as-cones
ARIN TAL issue needs addressing

## Slide 28: Conclusion
Notes: Mention lack of operator experience – but is solvable